## Slide 1: STM32
Training Hands on and Tools overview

## Slide 2: Tools Overview
Evaluation Boards
Free IDEs
  AC6
  CoIDE
  Keil (M0/M0+)
  mbed
Ecosystem
  STM32CubeMX
  STLink Utility
  ST Visual Programmer (STVP)
  STM32 Flash Loader Demonstrator
  Dfuse
  STM Studio

## Slide 3: Broad Range of Development Tools
STM32 Nucleo expansion boards
From full evaluation to open hardware
Flexible prototyping
Key feature prototyping
Full feature evaluation
STM32 Nucleo
Discovery kits
Evaluation boards
3rd parties
www.st.com/stm32nucleo
www.st.com/stm32discovery
Specialized functionality add-on
www.st.com/x-nucleo
Connectivity, Sensors…
Notes: Various types of development boards enable you to get started with the STM32 microcontrollers.
* The STM32 Nucleo boards provide an affordable and flexible way for anyone to try out new ideas and build prototypes with a wide choice of specialized expansion boards.
* The Discovery kits enable users to seamlessly exercise key features of STM32 products, while the Evaluation board exposes all MCU functionalities.
All these development boards include an integrated debugger/programmer as well as a comprehensive software library with examples that help developers to take davantage of STM32 capabilities.

## Slide 4: Comprehensive choice of IDEs
Monitor
Generate Code
Compile & Debug
STM32CubeMX
Partners IDEs
STMStudio
Free IDE

## Slide 5: System Workbench for STM32
Free Eclipse-based flexible software development environment :
  Covers the full range of STM32 mcus and associated boards (Nucleo, Discovery, Eval).
  Comprehensive support for STM32 firmware (Standard Peripheral library or Cube HAL).
  Customisation enabled through Eclipse plug-ins (SVN, EGit…).
Key features :
  GCC C/C++ compiler.
  GDB-based debugger.
  ST-Link support.
  Multi-OS support : Windows, Linux & OSX (Q2’2015).
  No code size limit.
  SW4STM32 project format will be supported by CubeMX.

## Slide 6: System Workbench for STM32
How to download SW4STM32 ?
  Go to associated collaborative site at www.openstm32.org
  Register to this site.
  Get installation instructions at the Documentation > System Workbench page.
  Proceed with immediate download of the toolchain.
Technical support :
  Handled through the associated Openstm32 website.
  Documentation, forum, blog, trainings are available to provide assistance to users.

## Slide 7: CoIDE
Free Eclipse-based simplified software development environment:
  Supports all STM32 mcus and Nucleo boards.
  Supports STM32Cube firmware (HAL).
  Download and Technical support available through collaborative site at www.coocox.org
Key features :
  GCC C/C++ compiler.
  GDB-based debugger.
  No code size limit.
  ST-Link support.
  English and Chinese languages are supported.

## Slide 8: MDK-ARM
Comprehensive software development environment for Cortex-M devices :
  Free version for ST supports all STM32F0 and STM32L0 mcus and associated boards (Nucleo, Discovery, Eval).
  Comprehensive support for STM32 firmware (Std Peripheral library or Cube HAL).
  Technical support available through the ARM Connected Community site at community.arm.com
Key features :
  ARM C/C++ compiler.
  uVision IDE, debugger and simulation environment.
  CMSIS-compliant.
  ST-Link support.
  English, Chinese, Japanese, Korean languages are supported.
  The setup of peripherals configured by CubeMX is directly exported to MDK.

## Slide 9: Free MDK-ARM for ST
Free licenses for STM32 devices based on Cortex-M0/M0+ cores :
  Applicable immediately to all STM32F0 and STM32L0 mcus.
  PC-locked multi-year licenses.
  No code size limit.
  Multiple language support.
  Technical support included.
Direct download from Keil website :
  No limit of number of downloads by customer.
  Direct access to configuration files for STM32 and associated boards.
  Free access to MDK-ARM periodic updates.
How to get free MDK-ARM licenses for STM32F0 and STM32L0 ?
  Go to Keil website at : www.keil.com/mdk-st
  Download MDK-ARM toolchain.
  Activate the free license using this Product Serial Number (PSN) : U1E21-CM9GY-L3G4L

## Slide 10: Comprehensive choice of STM32 free IDEs
Q2’2015
Q2’2015
Free licenses for all STM32 microcontrollers
Free licenses for STM32F0 & STM32L0
Free access to all STM32Nucleo users
System Workbench
CoIDE
MDK-ARM

## Slide 11: STM32Snippets: A Low Level Coding Package

## Slide 12: STM32 Embedded Software Offer - Overview
ST Offering. Free
Partners Offer
Abstraction Level
Portability Level
STM32Snippets
Standard Peripheral Libraries
STM32Cube
Mbed Core
« C » partners
Micrium, SEGGER,
HCC, ….
Virtual Machines
With partners
.Net, Java
IS2T, Oracle, Mountainer, .…
STM32 Device
-specific
f.i.: STM32F072
STM32 Series
-specific
f.i.: STM32F1
STM32 Family
-specific
Cortex-M based
MCUs
-specific
Any MCU
Beyond MCU
world

## Slide 13: STM32Snippets
What is it ?
  A collection of code examples, directly based on STM32 peripheral registers, available in documentation and as software bundles
Target Audience
  low level embedded system developers, typically coming from an 8 bit background, used to assembly or C with little abstraction
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
 | +++ |  |  | +
Features:
  Highly Optimized
  Register Level Access
  Small code expressions
  Closely follows the reference manual
  Debugging close to register level
Limitations:
  Specific to STM32 devices, not portable directly between series
  Not matching complex peripherals such as USB
  Lack of abstraction means developers must understand peripheral operation at register level
  Available (today) on STM32 L0 and F0 series

## Slide 14: Standard Peripheral Libraries (SPL)
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
++ | ++ | + | ++ | +++
What is it ?
  Collection of C Libraries covering STM32 peripherals
Target Audience
  Embedded systems developers with procedural C background. All existing STM32 customer base prior to the STM32Cube launch, willing to keep same supporting technology for future projects, and same STM32 series.
Features:
  Average optimization, fitting lots of situations
  No need for direct register manipulation
  100% coverage of all peripherals
  Easier debugging of procedural code
  Extensions for complex middleware such as USB/TCP-IP/Graphics/Touch Sense
Limitations:
  Specific to certain STM32 series.
  No common HAL API prevents application portability between series
  Middleware libraries may not be unified for each series
  Doesn’t support forward STM32 series starting with STM32 L0 and F7

## Slide 15: STM32Cube - Embedded software
STM32Cube
STM32 Hardware abstraction layer
STM32Cube
Middleware
User code
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
+++ | + | ++ | +++ | +++
What is it ?
  Full featured packages with drivers, USB, TCP/IP, Graphics, File system and RTOS
  Set of common application programming interfaces, ensuring high portability inside whole STM32 family
Target Audience
  Embedded system developers with a strong structured C background. New customers looking for a fast way to evaluate STM32 and easy portability
Limitations:
  May be challenging to low level C programmers in the embedded space.
  Higher portability creates bigger software footprints or more time spent executing adaptation code
  Not Available (today) on STM32 F1 series
Features:
  High level and functional abstraction
  Easy port from one series to another
  100% coverage of all peripherals
  Integrates complex middleware such as USB/TCP-IP/Graphics/Touch Sense/RTOS
  Can work with STM32CubeMX tool on the PC to generate initialization code

## Slide 16: ST Embedded software offer – Comparison
Offer | Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
STM32Snippets |  | +++ |  |  | +
Standard Peripheral Library | ++ | ++ | + | ++ | +++
STM32Cube | +++ | + | ++ | +++ | +++

## Slide 17: ST Embedded software offer - Positioning
STM32Snippets
Standard Peripheral Libraries
STM32 Device
-specific
f.i.: STM32F072
STM32 Series
-specific
f.i.: STM32F1
STM32 Family
Portability Level
STM32Cube HAL
(Hardware Abstraction Layer)
TCP/IP
FAT
File
Sys.
Gfx
USB
Host / Device
STM32Cube Middleware level
RTOS
STM32Cube Embedded Software packages
Touch
Abstraction Level
TCP/IP
FAT
File
Sys.
Gfx
USB
Host / Device
RTOS
Touch
Libraries, released independently

## Slide 18: Availability
Offer | Available for STM32 |  |  |  |  |  |  |  | 
STM32Snippets | Now | N.A. | N.A. | N.A. | N.A. | N.A. | Now | N.A. | N.A.
Standard Peripheral Library | Now | Now | Now | Now | Now | N.A. | N.A. | Now | N.A.
STM32Cube | Now | Now | Now | Now | Now | June 15 | Now | Now | Sept 15

## Slide 19: STM32Cube Ecosystem

## Slide 20: STM32CubeTM Introduction
STM32CubeTM includes:
  A configuration tool, STM32CubeMX generating initialization code from user choices
  Firmware offering, delivered per series (like STM32CubeF4) with:
    An STM32 Abstraction Layer embedded software: STM32Cube HAL
    A consistent set of Middleware: RTOS, USB, TCP/IP, Graphics, …
STM32Cube HAL: Portable API within all series - Middleware stacks when applicable: RTOS, USB, TCP/IP, Graphics, …
STM32CubeMX
STM32CubeF3
STM32CubeF2
STM32CubeF4
STM32CubeF1
STM32CubeF0
STM32CubeL1
Initialization Code generation based on user choices
20
STM32CubeL0

## Slide 21
Pinout Wizard
Clock Tree wizard
Peripherals & Middleware
Wizard
Power Consumption
Wizard
STM32CubeMX
21

## Slide 22
STM32CubeMX
Generates Initialization C Code
based on user choices !
22

## Slide 23: STM32CubeMX: MCU Selector
Filter by:
Series
Line
Package
Peripherals

## Slide 24: STM32CubeMX: Pin-out configuration
Pinout from:
  Peripheral tree
  Manually
Automatic signal remapping
Management of dependencies between peripherals

## Slide 25: STM32CubeMX: Clock tree
Immediate display of all clock values
Management of all clock constraints
Highlight of errors

## Slide 26: STM32CubeMX: Peripheral configuration
Global view of used peripherals and middleware
Highlight of configuration errors
Manage:
  GPIO
  Interrupts
  DMA

## Slide 27: Power consumption calculator
Power step definitions
Battery selection
Creation of consumption graph
Display of
  Average consumption
  Average DMIPS
  Battery lifetime

## Slide 28: STM32Cube Supporting all STM32 MCUs
Generate your configuration code with the STM32Cube and you can focus on your added-value software !
  4 configuration wizards: pinout, clock, peripherals & middleware, power consumption
  Portable Hardware Abstraction layer, from series to others
  Middleware with RTOS, USB, TCP/IP, File System, Graphics , Touch sensing…
www.st.com/stm32cube

## Slide 29: STM32Cube Main Features
STM32Cube gathers together, in a single package, all the generic and highly portable embedded software components required to develop an application on STM32 microcontrollers.
The package includes a low level hardware abstraction layer (HAL) that covers the microcontroller hardware, together with an extensive set of examples running on STMicroelectronics boards.
It also contains a set of middleware components (*) with the corresponding examples. They come with very permissive license terms:
  Full USB Host and Device stack supporting many classes.
    Host Classes: HID, MSC, CDC, Audio, MTP
    Device Classes: HID, MSC, CDC, Audio, DFU
  Graphics
    STemWin, a professional graphical stack solution available in binary format and based on the emWin solution from ST's partner SEGGER
    LibJPEG, an open source implementation on STM32 for JPEG images encoding and decoding.
  CMSIS-RTOS implementation with FreeRTOS open source solution
  FAT File system based on open source FatFS solution
  TCP/IP stack based on open source LwIP solution
  SSL/TLS secure layer based on open source PolarSSL
A demonstration implementing all these middleware components is also provided
(*) middleware components availability depends on STM32 Series
Notes: * All-in one package
*

## Slide 30: STM32Cube Documentation
Generic doc
Generic doc
Generic doc
Generic doc
Generic doc
Generic doc
Generic doc
Generic doc
Series specific doc
Series specific doc

## Slide 31: STM32Cube FW Package Organization

## Slide 32: STM32Cube Examples Overview
For each board, a set of examples are provided with preconfigured projects for EWARM, MDK-ARM and TrueSTUDIO toolchains.
The right side figure shows the projects structure for STM324xG-EVAL board, which is identical for other boards.
The examples are classified depending on the STM32Cube level they apply to, and are named as below:
  examples in level 0 are called Examples, that uses HAL drivers without any Middleware component
  examples in level 1 are called Applications, that provides typical use cases of each Middleware component
  examples in level 2 are called Demonstration, that implements all the HAL, BSP and Middleware components
Template project is provided to build quickly any firmware application on a given board.
All examples have the same structure,
  \Inc folder that contains all header files
  \Src folder for the sources code
  \EWARM, \MDK-ARM and \TrueSTUDIO folders contain the preconfigured project for each toolchain.
  readme.txt describing the example behavior and needed environment to make it working

## Slide 33: Software Development – Toolchains
Many possible Development Toolchains directly supporting STM32
Many open source solutions exist, while Commercial solutions do all have some free options, either time-limited or code size-limited
Commercial solutions:
  IAR EWARM
  Keil MDK-ARM
  Atollic TrueStudio
  Rowley CrossWorks
  Raisonance Ride
  Altium Tasking
  …
Free or Open source solutions:
  Embest CooCox
  SEGGER emIDE
  Yagarto
  …

## Slide 34: STM32 ST-LINK Utility

## Slide 35: STM32 ST-LINK Utility
Standalone software tool allows in-system programming of STM32 devices
  Supports Binary, Hex and Motorola S-Record file formats
Allows programming option bytes
Supports ST-LINK/V2
Command line version available for usage with batch files and small quantity production
  ST-LINK_CLI.exe
  Supports multiple ST-LINK/V2 connected to same PC
User manual UM0892

## Slide 36: ST Visual Programmer

## Slide 37: STVP
Free software that supports Motorola S19 and Intel HEX formats
Load, Edit and Save executable and/or data files generated by the Assembler/Linker or C compilers
Erase, Program, View and Verify device Flash memory contents
Project mode to automate all configuration and programming tasks
Programming Toolkit with C/C++ source files for creating a programming application based STVP
STVP supports microcontroller programming via a complete range of hardware development tools and dedicated programmers, including:
  ST-LINK in-circuit debugger/programmer for STM8 and STM32

## Slide 38: STM32 FLASH LOADER DEMONSTRATOR

## Slide 39: FLASH LOADER DEMONSTRATOR
Illustrate the System Memory boot loader capabilities
The Flash loader demonstrator is designed to work with all STMicroelectronics devices that support the system memory boot mode UART protocol

## Slide 40: DFUSE

## Slide 41: DFUSE
Perform the upgrade operation with some requires, such as:
  Product identifier
  Vendor identifier
  Firmware version
  Alternate setting number (Target ID) of the target to be used,
These information makes the upgrade targeted and more secure.
To add this information, a new file format should be used, to be called DFU file format

## Slide 42: STMSTUDIO

## Slide 43: STMSTUDIO
STM Studio is a non-intrusive tool, preserving the real-time behavior of applications.
STM Studio perfectly complements traditional debugging tools to fine tune applications.
It is well suited for debugging applications which cannot be stopped, such as motor control applications.
Connects to any STM32 via ST-LINK (JTAG or SWD protocols), reads on-the-fly (non intrusive) variables from RAM while application is running

## Slide 44: STM32F0 Labs

## Slide 45: System Peripherals
GPIO & EXTI (1.1)
  GPIO lab (1.1.1)
  EXTI lab (1.1.2)
1

## Slide 46: Basic communication peripherals
UART (2.1)
  UART Poll lab (2.1.1)
  UART Interrupt lab (2.1.2)
  UART DMA lab (2.1.3)
SPI (2.2)
  SPI Poll lab (2.2.1)
  SPI Interrupt lab (2.2.2)
I2C (2.3)
  I2C Interrupt lab (2.3.2)
2

## Slide 47: Timing peripherals
TIM (3.1)
  TIM Interrupt lab (3.1.1)
3

## Slide 48: Analog peripherals
ADC (4.1)
  ADC Interrupt lab (4.1.2)
4

## Slide 49: Control peripherals
CRC(5.1)
  TIM Interrupt lab (5.1.1)
5

## Slide 50: Application
IAP
  Demonstration of IAP based in AN4657
    http://www.st.com/web/en/catalog/tools/FM147/CL1794/SC961/SS1743/LN1920/PF262163?s_searchtype=keyword#
6

## Slide 51: 1.1.1 GPIO Lab

## Slide 52: Configure GPIO for LED toggling
Objective
  Learn how to setup pin and GPIO port in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure GPIO pin in CubeMX and Generate Code
  Add in to project HAL_Delay function and HAL_GPIO_Toggle function
  Verify the correct functionality on toggling LED
1.1.1

## Slide 53: Configure GPIO for LED toggling
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
Configure LED pin as GPIO_Output
1.1.1

## Slide 54: Configure GPIO for LED toggling
For debug purpose is recommended to select debug pins SWD or JTAG
  Select can be done in TAB>Pinout>SYS
  On discovery is available only SWD option
  If SWD/JTAG is not selected and the Set all free pins as analog (MENU>Project>Settings>TAB>Code Generator) is selected, debug is not possible
1.1.1

## Slide 55: Configure GPIO for LED toggling
Clock Configuration
  TAB>Clock Configuration
We can easily setup STM32 clocks
1.1.1

## Slide 56: Configure GPIO for LED toggling
The Clock configuration tree is interactive version of tree from RM
RM0360 Chapter 7 Reset and clock control Page 80
1.1.1

## Slide 57: Configure GPIO for LED toggling
Clock Configuration overview 1
Clock sources
  Internal oscillators
Internal oscillators
1.1.1

## Slide 58: Configure GPIO for LED toggling
Clock Configuration overview 3
Clock sources
  Internal oscillators
  External clock sources
External clock sources
1.1.1

## Slide 59: Configure GPIO for LED toggling
GPIO Configuration
  TAB>Configuration>System>GPIO
1.1.1

## Slide 60: Configure GPIO for LED toggling
GPIO(Pin) Configuration
  Select Push Pull mode
  No pull-up and pull-down
  Output speed to HIGH Is important for faster peripheries like SPI, USART
  Button OK
1.1.1

## Slide 61: Configure GPIO for LED toggling
GPIO(Pin) output speed configuration
  Change the rising and falling edge when pin change state from high to low or low to high
  Higher GPIO speed increase EMI noise from STM32 and increase STM32 consumption
  It is good to adapt GPIO speed with periphery speed. Ex.: Toggling GPIO on 1Hz is LOW optimal settings, but SPI on 45MHz the HIGH must be set
LOW
HIGH
LOW
HIGH
LOW
HIGH
GPIO output LOW speed
GPIO output MEDIUM speed
GPIO output HIGH speed
1.1.1

## Slide 62: Configure GPIO for LED toggling
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
1.1.1

## Slide 63: Configure GPIO for LED toggling
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinite loop while(1){ }
For toggling we need to use this functions
  HAL_HAL_Delay which create specific delay
  HAL_GPIO_WritePin or HAL_GPIO_TogglePin
1.1.1

## Slide 64: Configure GPIO for LED toggling
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinite loop while(1){ }
For toggling we need to use this functions
  HAL_HAL_Delay which create specific delay
  HAL_GPIO_WritePin or HAL_GPIO_TogglePin
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_5, GPIO_PIN_SET);
HAL_Delay(500);
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_5, GPIO_PIN_RESET);
HAL_Delay(500);
}
/* USER CODE END 3 */
1.1.1

## Slide 65: 1.1.2 EXTI lab

## Slide 66: Configure EXTI to turn on LED
Objective
  Learn how to setup input pin with EXTI in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure GPIO and EXTI pin in CubeMX and Generate Code
  Add into project Callback function and function which turn on led
  Verify the correct functionality by pressing button which turns on LED
1.1.2

## Slide 67: Configure EXTI to turn on LED
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
Configure LED pin as GPIO_Output
1.1.2

## Slide 68: Configure EXTI to turn on LED
Configure Button pin as GPIO_EXTIX
1.1.2

## Slide 69: Configure EXTI to turn on LED
In order to run on maximum frequency, setup clock system
Details in lab 0
1.1.2

## Slide 70: Configure EXTI to turn on LED
GPIO Configuration
  TAB>Configuration>System>GPIO
1.1.2

## Slide 71: Configure EXTI to turn on LED
GPIO(Pin) Configuration
  Select External Interrupt Mode with Faling edge trigger detection
  No pull-up or pull-down
  Button OK
1.1.2

## Slide 72: Configure EXTI to turn on LED
NVIC Configuration
  We need to enable interrupts for EXTI
  TAB>Configuration>System>NVIC
1.1.2

## Slide 73: Configure EXTI to turn on LED
NVIC Configuration
  Enable interrupt for EXTI Line4_15
  Button OK
1.1.2

## Slide 74: Configure EXTI to turn on LED
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
1.1.2

## Slide 75: Configure EXTI to turn on LED
HAL Library work flow 1
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
Generated by CubeMX
1.1.2

## Slide 76: Configure EXTI to turn on LED
HAL Library work flow 2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
MX_GPIO_Init
inside main.c
1.1.2

## Slide 77: Configure EXTI to turn on LED
HAL Library working flow 3
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
inside stm32f0xx_it.c
1.1.2

## Slide 78: Configure EXTI to turn on LED
HAL Library work flow 4
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
User must define Callback it is declared by default as empty weak
1.1.2

## Slide 79: Configure EXTI to turn on LED
HAL Library work flow 5
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
Usually in main.c between /* USER CODE BEGIN */
tags
1.1.2

## Slide 80: Configure EXTI to turn on LED
HAL Library work flow summary
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI4_15_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI4_15_IRQHandler
2. init GPIO
1. init NVIC
3. create edge
4. EXTI interrupt handler
5. HAL EXTI interrupt handler
6. HAL EXTI callback
HAL files clearing flags, check errors, …
1.1.2

## Slide 81: Configure EXTI to turn on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on we need to use this functions
  HAL_GPIO_WritePin
1.1.2

## Slide 82: Configure EXTI to turn on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on we need to use this functions
  HAL_GPIO_WritePin
/* USER CODE BEGIN 4 */
void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
{
if(GPIO_Pin == GPIO_PIN_13) {
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_5, GPIO_PIN_SET);
} else {
__NOP();
}
}
/* USER CODE END 4 */
1.1.2

## Slide 83: 1.3.1 Data transfer over DMA lab

## Slide 84: Use DMA in M2M transfer
Objective
  Learn how to setup DMA transfer in CubeMX
  Create simple DMA memory to memory transfer from RAM to RAM
Goal
  Use CubeMX and Generate Code with DMA
  Learn how to setup the DMA in HAL
  Verify the correct functionality by comparing transferred buffers
1.3.1

## Slide 85: Use DMA in M2M transfer
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQF64 > STM32F030R8
For DMA we don’t need to configure any pins
1.3.1

## Slide 86: Use DMA in M2M transfer
In order to run on maximum frequency, setup clock system
Details in lab 0
1.3.1

## Slide 87: Use DMA in M2M transfer
DMA configuration
  TAB>Configuration
  System>DMA
  TAB>DMA1
  Button ADD
1. TAB > Configuration
2. System DMA
3. TAB>DMA 1
4. Add DMA channel
1.3.1

## Slide 88: Use DMA in M2M transfer
DMA configuration
  Select MEMTOMEM DMA request
  Normal mode
  Increment source and destination address
  Byte data width
  Button OK
1. MEMTOMEM
2. Normal mode
3. Increment addresses
5. OK
1.3.1
4. Byte

## Slide 89: Use DMA in M2M transfer
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
1.3.1

## Slide 90: Use DMA in M2M transfer
Start process DMA (same for TIM, ADC)
  Non blocking start process
  The end of the process must be checked by polling
Peripheral Initializations
Start Process
(HAL_DMA_Start)
Poll for process complete
(HAL_DMA_PollForTransfer)
1. init DMA
2. Start DMA
3. DMA transfer data
4. Check if transfer is complete
1.3.1

## Slide 91: Use DMA in M2M transfer
Return values
  Most of CubeMX functions have return values, which indicate, if operation was successful, timeout occurs of function end with error
  Is recommended handle this return values to be sure that program working as expected
Ex: Poll for process complete
(HAL_DMA_PollForTransfer)
HAL_ERROR
HAL_OK
HAL_BUSY
DMA transfer was successfully finished and data was transferred to destination without error
1.3.1

## Slide 92: Use DMA in M2M transfer
Return values
  Most of CubeMX functions have return values, which indicate, if operation was successful, timeout occurs of function end with error
  Is recommended handle this return values to be sure that program working as expected
Ex: Poll for process complete
(HAL_DMA_PollForTransfer)
HAL_ERROR
HAL_OK
HAL_BUSY
Error occurs during DMA transfer you use HAL_DMA_GetError for details what happened
1.3.1

## Slide 93: Use DMA in M2M transfer
Return values
  Most of CubeMX functions have return values, which indicate, if operation was successful, timeout occurs of function end with error
  Is recommended handle this return values to be sure that program working as expected
Ex: Poll for process complete
(HAL_DMA_PollForTransfer)
HAL_ERROR
HAL_OK
HAL_BUSY
DMA transfer in progress, user can only abort the transfer
1.3.1

## Slide 94: Use DMA in M2M transfer
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
HAL functions for DMA
  HAL_DMA_Start(DMA_HandleTypeDef *hdma, uint32_t SrcAddress, uint32_t DstAddress, uint32_t DataLength)
  HAL_DMA_PollForTransfer(DMA_HandleTypeDef *hdma, uint32_t CompleteLevel, uint32_t Timeout)
1.3.1

## Slide 95: Use DMA in M2M transfer
We create two buffers
  One with source data
  Second as destination buffer
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
/* USER CODE END 0 */
1.3.1

## Slide 96: Use DMA in M2M transfer
HAL_DMA_Start start the M2M data transfer
HAL_DMA_PollForTransfer check if the transfer ends successfully
Remember to extern the hdma_memtomem_dma1_channel1 structure
/* USER CODE BEGIN 2 */
HAL_DMA_Start(& hdma_memtomem_dma1_channel1, (uint32_t) (Buffer_Src), (uint32_t) (Buffer_Dest), 10);
while(HAL_DMA_PollForTransfer(&hdma_memtomem_dma1_channel1, HAL_DMA_FULL_TRANSFER, 100) != HAL_OK)
{
__NOP();
}
/* USER CODE END 2 */
1.3.1

## Slide 97: 1.3.2 Data transfer over DMA with interrupt lab

## Slide 98: Use DMA M2M with interrupt
Objective
  Learn how to setup DMA transfer with interrupt in CubeMX
  Create simple DMA memory to memory transfer from RAM to RAM
Goal
  Use CubeMX and Generate Code with DMA
  Learn how to setup the DMA in HAL
  Verify the correct functionality by comparing transferred buffers
1.3.2

## Slide 99: Use DMA M2M with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQF64 > STM32F030R8
For DMA we don’t need to configure any pins
1.3.2

## Slide 100: Use DMA M2M with interrupt
In order to run on maximum frequency, setup clock system
Details in lab 0
1.3.2

## Slide 101: Use DMA M2M with interrupt
DMA configuration
  TAB>Configuration
  System>DMA
  TAB>DMA1
  Button ADD
1. TAB > Configuration
2. System DMA
3. TAB>DMA 1
4. Add DMA channel
1.3.2

## Slide 102: Use DMA M2M with interrupt
DMA configuration
  Select MEMTOMEM DMA request
  Normal mode
  Increment source and destination address
  Byte data width
  Button OK
1. MEMTOMEM
2. Normal mode
3. Increment addresses
5. OK
1.3.2
4. Byte

## Slide 103: Use DMA M2M with interrupt
DMA configuration
  System > NVIC
  Enable DMA1 Stream interrupt
  Button OK
3. Enable DMA1 interrupts
2. System > NVIC
4. OK
1.3.2

## Slide 104: Use DMA M2M with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
1.3.2

## Slide 105: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
DMA1_Channel1_IRQHandler
1.3.2

## Slide 106: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated by CubeMX
1.3.2
DMA1_Channel1_IRQHandler

## Slide 107: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Defined by user
1.3.2
DMA1_Channel1_IRQHandler

## Slide 108: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated in main.c
1.3.2
DMA1_Channel1_IRQHandler

## Slide 109: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
We recommend to use it in main.c
1.3.2
DMA1_Channel1_IRQHandler

## Slide 110: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
User defined functions. The user must define functions by himself and put function names into DMA structure
1.3.2
DMA1_Channel1_IRQHandler

## Slide 111: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated in stm32f0xx_it.c
1.3.2
DMA1_Channel1_IRQHandler

## Slide 112: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Defined in stm32f0xx_hal_dma.c
1.3.2
DMA1_Channel1_IRQHandler

## Slide 113: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Start DMA buffer transfer
Not blocking function program can continue
1.3.2
DMA1_Channel1_IRQHandler

## Slide 114: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Interrupt indicate DMA process is half/complete or error was detected
1.3.2
DMA1_Channel1_IRQHandler

## Slide 115: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Process interrupt information
1.3.2
DMA1_Channel1_IRQHandler

## Slide 116: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Data correctly transferred
Complete callback function
1.3.2
DMA1_Channel1_IRQHandler

## Slide 117: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Error was detected
Error callback function
1.3.2
DMA1_Channel1_IRQHandler

## Slide 118: Use DMA M2M with interrupt
HAL Library DMA with IT flow
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
1. DMA init
2. DMA transfer start
3. DMA transfer complete or error
4. HAL DMA management
5. DMA transfer was correct
5. Error in DMA transfer
1.3.2
DMA1_Channel1_IRQHandler

## Slide 119: Use DMA M2M with interrupt
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
DMA callback function
  We need to add the name of callback function into DMA structure
HAL functions for DMA
  HAL_DMA_Start_IT(DMA_HandleTypeDef *hdma, uint32_t SrcAddress, uint32_t DstAddress, uint32_t DataLength)
1.3.2

## Slide 120: Use DMA M2M with interrupt
We create two buffers
  One with source data
  Second as destination buffer
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
/* USER CODE END 0 */
1.3.2

## Slide 121: Use DMA M2M with interrupt
DMA callback creation function prototype
DMA complete callback with nop where we can put breakpoint
/* USER CODE BEGIN 4 */
void XferCpltCallback(DMA_HandleTypeDef *hdma)
{
__NOP();//we reach this only if DMA transfer was correct
}
/* USER CODE END 4 */
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
void XferCpltCallback(DMA_HandleTypeDef *hdma);
/* USER CODE END 0 */
1.3.2

## Slide 122: Use DMA M2M with interrupt
DMA Start
  Before we start the DMA with interrupt we need to set the callback into DMA structure
  Then is possible use the HAL_DMA_Start_IT to begin DMA transfer
/* USER CODE BEGIN 2 */
hdma_memtomem_dma1_channel1.XferCpltCallback=&XferCpltCallback;
HAL_DMA_Start_IT(&hdma_memtomem_dma1_channel1,(uint32_t)Buffer_Src,(uint32_t)Buffer_Dest,10);
/* USER CODE END 2 */
1.3.2

## Slide 123: 2.1.1 UART Poll lab

## Slide 124: Simple UART communication
Objective
  Learn how to setup UART in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Work in pairs, one will create transmitter and second receiver
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART without interrupts
  Verify the correct functionality
2.1.1

## Slide 125: Simple UART communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
2.1.1

## Slide 126: Simple UART communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX UART selection
  Select USART2 in asynchronous mode
  Select PA2 and PA3 for USART2 if weren't selected
2.1.1

## Slide 127: Simple UART communication
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.1

## Slide 128: Simple UART communication
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART2
2.1.1

## Slide 129: Simple UART communication
CubeMX USART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.1

## Slide 130: Simple UART communication
CubeMX USART GPIO configuration check:
  On high baud rate set the GPIO speed to HIGH
  Set the HIGH output speed Button OK
2.1.1

## Slide 131: Simple UART communication
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.1

## Slide 132: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL_UART_Init(&huart2);
Init UART2 structure
HAL Library init flow
Peripheral Initializations
MX_USART2_UART_Init();
CubeMX UART init start in main.c file
2.1.1

## Slide 133: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
1. We need init UART2
2.1.1
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 134: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
1. We need init UART2
CubeMX create for us function which handle UART initialization
2.1.1
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 135: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
1. We need init UART2
2. Call UART2 init function
2.1.1
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 136: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
2. Call UART2 init function
CubeMX fill the UART structure with parameters which we choose in Configuration window
2.1.1
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 137: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
2. Call UART2 init function
3. Store UART2 configuration into structure
2.1.1
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 138: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
3. Store UART1 configuration into structure
Function wrote parameters from structure into UART1 registers
2.1.1
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 139: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
3. Store UART1 configuration into structure
4. Write to UART2 registers
Optional callback from HAL_UART_Init function, be default empty weak function
2.1.1
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 140: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
3. Store UART1 configuration into structure
4. Write to UART2 registers
CubeMX configure here UART1 GPIOs and enable UART2 clock system
2.1.1
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 141: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
4. Write to UART2 registers
CubeMX configure here UART1 GPIOs and enable UART2 clock system and NVIC
5. UART2 init callback
2.1.1
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 142: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
3. Store UART1 configuration into structure
4. Write to UART2 registers
5. UART2 init callback
6. UART2 GPIOS, NVIC and RCC init
2.1.1
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 143: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL Library init flow
Peripheral Initializations
2. Call UART1 init function
7. Next periph init or user code
2.1.1
4. Write to UART2 registers
5. UART2 init callback
6. UART2 GPIOS, NVIC and RCC init
2. Call UART2 init function
3. Store UART2 configuration into structure
1. We need init UART2
HAL_UART_Init(&huart2);
Init UART2 structure
MX_USART2_UART_Init();

## Slide 144: Simple UART communication
HAL Library transmit flow
Generated by CubeMX
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_UART_Transmit
HAL_BUSY
2.1.1

## Slide 145: Simple UART communication
HAL Library transmit flow
Created by user
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_UART_Transmit
HAL_BUSY
2.1.1

## Slide 146: Simple UART communication
HAL Library receive flow
Generated by CubeMX
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_UART_Receive
HAL_BUSY
2.1.1

## Slide 147: Simple UART communication
HAL Library receive flow
Created by user
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_UART_Receive
HAL_BUSY
2.1.1

## Slide 148: Simple UART communication
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinite while function
For transmit use function
  HAL_UART_Transmit(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size, uint32_t Timeout)
For receive use function
  HAL_UART_Receive(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size, uint32_t Timeout);
2.1.1

## Slide 149: Simple UART communication
Transmit solution
  Create data structure for data
  Call transmit function from while loop
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_UART_Transmit(&huart2,data,10,1000);
}
/* USER CODE END 3 */
/* USER CODE BEGIN 0 */
uint8_t data[]={0x30,0x31,0x32,0x33,0x34,0x35,0x36,0x37,0x38,0x39};
/* USER CODE END 0 */
2.1.1

## Slide 150: Simple UART communication
Receive solution
  Create data structure for data
  Call transmit function from while loop
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_UART_Receive(&huart2,data,10,1000);
}
/* USER CODE END 3 */
/* USER CODE BEGIN 0 */
uint8_t data[10];
/* USER CODE END 0 */
2.1.1

## Slide 151: 2.1.2 UART Interrupt lab

## Slide 152: Use UART with interrupt
Objective
  Learn how to setup UART with interrupts in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with interrupts
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART with interrupts
  Verify the correct functionality
2.1.2

## Slide 153: Use UART with interrupt
2.1.2
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX UART selection
  Select USART2 in asynchronous mode
  Select PA2 and PA3 for USART2 if weren't selected

## Slide 154: Use UART with interrupt
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.2

## Slide 155: Use UART with interrupt
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART2
2.1.2

## Slide 156: Use UART with interrupt
CubeMX UART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.2

## Slide 157: Use UART with interrupt
CubeMX USART configuration NVIC settings
  TAB>NVIC Settings
  Enable interrupts
  OK
2.1.2

## Slide 158: Use UART with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.2

## Slide 159: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Receive_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
USART2_IRQHandler
2.1.2

## Slide 160: Use UART with interrupt
HAL Library UART with IT transmit flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
2.1.2
USART2_IRQHandler

## Slide 161: Use UART with interrupt
HAL Library UART with IT transmit flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated by CubeMX
2.1.2
USART2_IRQHandler

## Slide 162: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Defined by user
2.1.2
USART2_IRQHandler

## Slide 163: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated in main.c and stm32f4xx_hal_msp.c
2.1.2
USART2_IRQHandler

## Slide 164: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
We recommend to use it in main.c
2.1.2
USART2_IRQHandler

## Slide 165: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Defined as __weak you can find name of this functions in stm32f0xx_hal_uart.c
2.1.2
USART2_IRQHandler

## Slide 166: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Generated in stm32f0xx_it.c
2.1.2
USART2_IRQHandler

## Slide 167: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Defined in stm32f0xx_hal_uart.c
2.1.2
USART2_IRQHandler

## Slide 168: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Send buffer over UART Not blocking function program can continue
2.1.2
USART2_IRQHandler

## Slide 169: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Interrupt indicate the data register is empty we can send more data or error was detected
2.1.2
USART2_IRQHandler

## Slide 170: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Process interrupt information
2.1.2
USART2_IRQHandler

## Slide 171: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Send more data if is buffer not empty
2.1.2
USART2_IRQHandler

## Slide 172: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
If data buffer is empty use Complete callback function
2.1.2
USART2_IRQHandler

## Slide 173: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
Or if error was detected use Error callback function
2.1.2
USART2_IRQHandler

## Slide 174: Use UART with interrupt
HAL Library UART with IT receive flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
1. UART2 init
2. UART2 send buffer
3. UART2 Tx register empty
4. Send more data or manage error
5. Buffer sent
5. Transmit error
2.1.2
USART2_IRQHandler

## Slide 175: Use UART with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_UART_Transmit_IT(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
For receive use function
  HAL_UART_Receive_IT(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
2.1.2

## Slide 176: Use UART with interrupt
Buffer definition
Sending and receiving methods
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0x30,0x31,0x32,0x33,0x34,0x35,0x36,0x37,0x38,0x39};uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_UART_Receive_IT(&huart2,rx_buff,10);
HAL_UART_Transmit_IT(&huart2,tx_buff,10);
/* USER CODE END 2 */
2.1.2

## Slide 177: Use UART with interrupt
Complete callback check
  We can put brakepoints on NOPs to watch if we send or receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//test if we reach this position
}
void HAL_UART_TxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//test if we reach this position
}
/* USER CODE END 4 */
2.1.2

## Slide 178: 2.1.3 UART DMA lab

## Slide 179: Use UART with DMA transfer
Objective
  Learn how to setup UART with DMA in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with DMA
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART with DMA
  Verify the correct functionality
2.1.3

## Slide 180: Use UART with DMA transfer
2.1.3
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX UART selection
  Select USART2 in asynchronous mode
  Select PA2 and PA3 for USART2 if weren't selected

## Slide 181: Use UART with DMA transfer
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.3

## Slide 182: Use UART with DMA transfer
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART2
2.1.3

## Slide 183: Use UART with DMA transfer
CubeMX USART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.3

## Slide 184: Use UART with DMA transfer
CubeMX USART configuration DMA settings
  TAB>DMA Settings
  Button ADD
2.1.3

## Slide 185: Use UART with DMA transfer
CubeMX USART configuration DMA Tx settings
  Set USART2_TX request
  Memory to peripheral direction
  Normal mode
  Byte data width
  Increment memory address
2.1.3

## Slide 186: Use UART with DMA transfer
CubeMX USART configuration DMA Rx settings
  Button ADD
  Set USART2_RX request
  Peripheral to memory direction
  Normal mode
  Byte data width
  Increment memory address
2.1.3

## Slide 187: Use UART with DMA transfer
CubeMX USART configuration NVIC settings
  TAB>NVIC Settings
  Enable DMA1 interrupts for USART2
  Button OK
2.1.3

## Slide 188: Use UART with DMA transfer
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.3

## Slide 189: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
2.1.3

## Slide 190: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Generated by CubeMX
2.1.3

## Slide 191: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Defined by user
2.1.3

## Slide 192: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Generated in main.c and stm32f0xx_hal_msp.c
2.1.3

## Slide 193: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
We recommend to use it in main.c
2.1.3

## Slide 194: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Generated in stm32f0xx_it.c
2.1.3

## Slide 195: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Defined in stm32f0xx_hal_dma.c and then linked to stm32f0xx_hal_uart.c
2.1.3

## Slide 196: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Receive buffer over UART with DMA Not blocking function program can continue
2.1.3

## Slide 197: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Interrupt indicate the DMA receive half/complete buffer or DMA error was detected
2.1.3

## Slide 198: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Process interrupt information from DMA and UART
2.1.3

## Slide 199: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
If data buffer is full HAL use Complete callback function
2.1.3

## Slide 200: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
Or if DMA error was detected use Error callback function
2.1.3

## Slide 201: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
1. UART2 and DMA1 init
2. UART2 receive buffer
3. DMA buffer full
4. Process interrupt
5. Buffer received
5. Receive error
2.1.3

## Slide 202: Use UART with DMA transfer
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_UART_Transmit_DMA(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
For receive use function
  HAL_UART_Receive_DMA(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
2.1.3

## Slide 203: Use UART with DMA transfer
Buffer definition
Sending and receiving methods with DMA
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_UART_Receive_DMA(&huart2,rx_buff,10);
HAL_UART_Transmit_DMA(&huart2,tx_buff,10);
/* USER CODE END 2 */
2.1.3

## Slide 204: Use UART with DMA transfer
Complete callback check
  We can put breakpoints on NOPs to watch if we receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//check if we receive all data
}
/* USER CODE END 4 */
2.1.3

## Slide 205: 2.2.1 SPI Poll lab

## Slide 206: Simple SPI communication
Objective
  Learn how to setup SPI in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure SPI in CubeMX and Generate Code
  Learn how to send and receive data over SPI without interrupts
  Verify the correct functionality
2.2.1

## Slide 207: Simple SPI communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
2.2.1

## Slide 208: Simple SPI communication
2.2.1
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX SPI selection
  Select SPI1 Full-Duplex Master
  Select PB5, PB4, PB3 for SPI1 if weren't selected

## Slide 209: Simple SPI communication
Hardware preparation
  Connect PB4 and PB5 together with jumper
Hardware loopback
2.2.1

## Slide 210: Simple SPI communication
In order to run on maximum frequency, setup clock system
Details in lab 0
2.2.1

## Slide 211: Simple SPI communication
CubeMX SPI configuration
  Tab>Configuration>Connectivity>SPI1
  Check the settings
  Button OK
  The CLK frequency with core on 48MHz is now 12MHz
  For this clock use HIGH GPIO speed
2.2.1

## Slide 212: Simple SPI communication
CubeMX SPI – GPIO configuration
  Tab>Configuration>System> >GPIO
  Tab>SPI1
  Seth High output speed
  Button OK
2.2.1

## Slide 213: Simple SPI communication
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.2.1

## Slide 214: Simple SPI communication
HAL Library transmit receive flow
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_SPI_TransmitReceive
HAL_BUSY
2.2.1

## Slide 215: Simple SPI communication
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For transmit and receive use function
  HAL_SPI_TransmitReceive(SPI_HandleTypeDef *hspi, uint8_t *pTxData, uint8_t *pRxData, uint16_t Size, uint32_t Timeout)
2.2.1

## Slide 216: Simple SPI communication
Transmit receive solution
  Create data structure for data
  Call transmit receive function
/* USER CODE BEGIN PV */
uint8_t tx_buffer[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buffer[10];
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
HAL_SPI_TransmitReceive(&hspi1,tx_buffer,rx_buffer,10,100);
/* USER CODE END 2 */
2.2.1

## Slide 217: 2.2.2 SPI Interrupt lab

## Slide 218: Use SPI with interrupt
Objective
  Learn how to setup SPI with interrupts in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with interrupts
Goal
  Configure SPI in CubeMX and Generate Code
  Learn how to send and receive data over SPI with interrupts
  Verify the correct functionality
2.2.2

## Slide 219: Use SPI with interrupt
2.2.2
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX SPI selection
  Select SPI1 Full-Duplex Master
  Select PB5, PB4, PB3 for SPI1 if weren't selected

## Slide 220: Use SPI with interrupt
Hardware preparation
  Connect PB4 and PB5 together with jumper
2.2.2
Hardware loopback

## Slide 221: Use SPI with interrupt
In order to run on maximum frequency, setup clock system
Details in lab 0
2.2.2

## Slide 222: Use SPI with interrupt
CubeMX SPI configuration
  Tab>Configuration>Connectivity>SPI1
  Check the settings
  Button OK
2.2.2

## Slide 223: Use SPI with interrupt
CubeMX SPI configuration
  TAB>NVIC Settings
  Enable SPI interrupt
  Button OK
2.2.2

## Slide 224: Use SPI with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.2.2

## Slide 225: Use SPI with interrupt
HAL Library SPI with IT transmit receive flow
Start process with interrupt generation at end of process
HAL_SPI_TransmitReceive_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_SPI_IRQHandler
end of process callback
HAL_SPI_TxRxCpltCallback
process Error callback
HAL_SPI_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
SPI1_IRQHandler
2.2.2

## Slide 226: Use SPI with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_SPI_TransmitReceive_IT(SPI_HandleTypeDef *hspi, uint8_t *pTxData, uint8_t *pRxData, uint16_t Size)
2.2.2

## Slide 227: Use SPI with interrupt
Buffer definition
Sending and receiving methods
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_SPI_TransmitReceive_IT(&hspi1,tx_buff,rx_buff,10);
/* USER CODE END 2 */
2.2.2

## Slide 228: Use SPI with interrupt
Complete callback check
  We can put breakpoints on NOPs to watch if we send or receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_SPI_TxRxCpltCallback(SPI_HandleTypeDef *hspi)
{
__NOP();
}
/* USER CODE END 4 */
2.2.2

## Slide 229: 2.2.3 SPI DMA lab

## Slide 230: Use SPI with DMA transfer
Objective
  Learn how to setup SPI with DMA in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with DMA
Goal
  Configure SPI in CubeMX and Generate Code
  Learn how to send and receive data over SPI with DMA
  Verify the correct functionality
2.2.3

## Slide 231: Use SPI with DMA transfer
2.2.3
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX SPI selection
  Select SPI1 Full-Duplex Master
  Select PB5, PB4, PB3 for SPI1 if weren't selected

## Slide 232: Use SPI with DMA transfer
2.2.3
Hardware preparation
  Connect PB4 and PB5 together with jumper
Hardware loopback

## Slide 233: Use SPI with DMA transfer
In order to run on maximum frequency, setup clock system
Details in lab 0
2.2.3

## Slide 234: Use SPI with DMA transfer
CubeMX SPI configuration
  Tab>Configuration>Connectivity>SPI1
  Check the settings
  Button OK
2.2.3

## Slide 235: Use SPI with DMA transfer
CubeMX SPI configuration DMA settings
  TAB>DMA Settings
  Button ADD
  SPI1_RX
  Memory increment
  Button ADD
  SPI1_Tx
  Memory increment
  Button OK
2.2.3

## Slide 236: Use SPI with DMA transfer
CubeMX SPI configuration NVIC settings
  TAB>NVIC Settings
  Enable DMA1 interrupts for SPI1
  Button OK
2.2.3

## Slide 237: Use SPI with DMA transfer
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.2.3

## Slide 238: Use SPI with DMA transfer
HAL Library SPI with DMA TX RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_SPI_TransmitReceive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_SPI_TxRxCpltCallback
process Error callback
HAL_SPI_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
DMA1_Stream_IRQHandler
2.2.3

## Slide 239: Use SPI with DMA transfer
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_SPI_TransmitReceive_DMA(SPI_HandleTypeDef *hspi, uint8_t *pTxData, uint8_t *pRxData, uint16_t Size)
2.2.3

## Slide 240: Use SPI with DMA transfer
Buffer definition
Sending and receiving methods
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_SPI_TransmitReceive_DMA(&hspi1,tx_buff,rx_buff,10);
/* USER CODE END 2 */
2.2.3

## Slide 241: Use SPI with DMA transfer
Complete callback check
  We can put breakpoints on NOPs to watch if we send or receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_SPI_TxRxCpltCallback(SPI_HandleTypeDef *hspi)
{
__NOP();
}
/* USER CODE END 4 */
2.2.3

## Slide 242: 2.3.1 I2C Poll lab

## Slide 243: Simple I2C communication
Objective
  Learn how to setup i2C in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Work in pairs, one will create I2C transmitter and second I2C receiver
Goal
  Configure I2C in CubeMX and Generate Code
  Learn how to send and receive data over I2C without interrupts
  Verify the correct functionality
2.3.1

## Slide 244: Simple I2C communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX SPI selection
  Select I2C3 Periphery
  Select PA8, PC9 for I2C3 if weren't selected
2.3.1

## Slide 245: Simple I2C communication
Hardware preparation
  Connect together PA8 and PC9 pins from both boards, and GND
2.3.1
Hardware connection PA8 <-> PA8
PC9<->PC9

## Slide 246: Simple I2C communication
CubeMX I2C configuration
  Tab>Configuration>Connectivity>I2C3
  Check the settings
  Define Slave address to 20
  Button OK
2.3.1

## Slide 247: Simple I2C communication
CubeMX I2C configuration
  Tab>GPIO Settings
  Check Pull-UP
  Check GPIO speed
2.3.1
Check if the Pull-UP resistor are necessary in case you are using external one
Check the GPIO speed
This two parameters can limit I2C maximum speed

## Slide 248: Simple I2C communication
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.3.1

## Slide 249: Simple I2C communication
Buffer definition
Master simple send and receive functions
/* USER CODE BEGIN PV */
/* Private variables
uint8_t data_tx[10]={1,2,3,4,5,6,7,8,9,0};
uint8_t data_rx[10];
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
HAL_Delay(100);
HAL_I2C_Master_Transmit(&hi2c3,20,data_tx,10,1000);
HAL_Delay(2);
HAL_I2C_Master_Receive(&hi2c3,20,data_rx,10,1000);
/* USER CODE END 2 */
2.3.1

## Slide 250: Simple I2C communication
Slave simple send and receive functions
During this example the SLAVE must begin the code execution first to be prepared on MASTER Receive/Send requests
/* USER CODE BEGIN 2 */
status1=HAL_I2C_Slave_Receive(&hi2c3,data_rx,10,10000);
status2=HAL_I2C_Slave_Transmit(&hi2c3,data_rx,10,10000);
/* USER CODE END 2 */
2.3.1

## Slide 251: 2.3.2 I2C Interrupt lab

## Slide 252: Use I2C with interrupt
Objective
  Learn how to setup I2C with interrupts in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with interrupts
Goal
  Configure I2C in CubeMX and Generate Code
  Learn how to send and receive data over I2C with interrupts
  Verify the correct functionality
2.3.2

## Slide 253: Use I2C with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX I2C selection
  Select I2C1 Periphery
  Select PB6, PB7 for I2C1 if weren't selected
2.3.2

## Slide 254: Use I2C with interrupt
CubeMX I2C configuration
  Tab>Configuration>Connectivity>I2C1
  Check the settings
  Define Slave address to 20
  Button OK
2.3.2

## Slide 255: Use I2C with interrupt
CubeMX I2C configuration
  Tab>GPIO Settings
  Check Pull-UP
  Check GPIO speed
2.3.2
Check if the Pull-UP resistor are necessary in case you are using external one
Check the GPIO speed
This two parameters can limit I2C maximum speed

## Slide 256: Use I2C with interrupt
CubeMX I2C configuration
  Tab>NVIC settings
  Enable interrupts
  Button OK
2.3.2

## Slide 257: Use I2C with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.3.2

## Slide 258: Use I2C with interrupt
Buffer definition
Master simple send and receive functions with interrupts
Master callbacks
/* USER CODE BEGIN PV */
/* Private variables
uint8_t data_tx[10]={1,2,3,4,5,6,7,8,9,0};
uint8_t data_rx[10];
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
HAL_I2C_Master_Transmit_IT(&hi2c1,20,data_tx,10);
HAL_Delay(2);
HAL_I2C_Master_Receive_IT(&hi2c1,20,data_rx,10);
/* USER CODE END 2 */
2.3.2
/* USER CODE BEGIN 4 */
void HAL_I2C_MasterTxCpltCallback(I2C_HandleTypeDef *hi2c){}
void HAL_I2C_MasterRxCpltCallback(I2C_HandleTypeDef *hi2c){}
/* USER CODE END 4 */

## Slide 259: Use I2C with interrupt
Slave receive
Slave transmit in callback
/* USER CODE BEGIN 2 */
HAL_I2C_Slave_Receive_IT(&hi2c1,data_rx,10);
/* USER CODE END 2 */
2.3.2
/* USER CODE BEGIN 4 */
void HAL_I2C_SlaveTxCpltCallback(I2C_HandleTypeDef *hi2c){
}
void HAL_I2C_SlaveRxCpltCallback(I2C_HandleTypeDef *hi2c){
HAL_I2C_Slave_Transmit_IT(&hi2c1,data_rx,10);
}
/* USER CODE END 4 */

## Slide 260: 3.2.1 TIM with interrupt lab

## Slide 261: Use TIM with interrupt
Objective
  Learn how to setup TIM with Interrupt in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Indicate TIM interrupt with LED toggle
Goal
  Configure TIM in CubeMX and Generate Code
  Learn how start timer and handle interrupt
  Verify the correct functionality
3.2.1

## Slide 262: Use TIM with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
CubeMX TIM selection
  Select TIM clock source Internal clock
  Enable GPIO for LED PA5
3.2.1

## Slide 263: Use TIM with interrupt
CubeMX TIM configuration
  Tab>Configuration>Control>TIM1
  Check the settings
3.2.1

## Slide 264: Use TIM with interrupt
CubeMX TIM configuration
  Tab>Parameter Settings
  Prescaler to 4799
  Counter period to 9999
  Together with 48MHz TIMER1 clock we get period 1Hz
3.2.1

## Slide 265: Use TIM with interrupt
CubeMX TIM configuration
  Tab>NVIC Settings
  Enable TIM1 Update interrupt
  Button OK
3.2.1

## Slide 266: Use TIM with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
3.2.1

## Slide 267: Use TIM with interrupt
HAL Library TIM with IT flow
Start process with interrupt generation at end of process
HAL_TIM_Base_Start_IT
TIM Initializations
including peripheral interrupt NVIC initializations
HAL_TIM_IRQHandler
process callback
HAL_TIM_PeriodElapsedCallback
process Error callback
HAL_TIM_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
TIM1_UP_TIM10_IRQHandler
3.2.1

## Slide 268: Use TIM with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For TIM start use function
  HAL_TIM_Base_Start_IT(TIM_HandleTypeDef *htim)
TIM callback
  void TIM1_UP_TIM10_IRQHandler(void)
GPIO LED toggle
  HAL_GPIO_TogglePin(GPIO_TypeDef* GPIOx, uint16_t GPIO_Pin)
3.2.1

## Slide 269: Use TIM with interrupt
Solution
  TIM start
  Callback handling
/* USER CODE BEGIN 2 */
HAL_TIM_Base_Start_IT(&htim1);
/* USER CODE END 2 */
/* USER CODE BEGIN 4 */
void HAL_TIM_PeriodElapsedCallback(TIM_HandleTypeDef *htim)
{
HAL_GPIO_TogglePin(GPIOA,GPIO_PIN_5);
}
/* USER CODE END 4 */
3.2.1

## Slide 270: 4.1.1 ADC Poll lab

## Slide 271: Use ADC in polling mode
Objective
  Use the DAC part from previous lab
  Learn how to setup ADC in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in poll in CubeMX and Generate Code
  Learn how to start ADC and measure the DAC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.1.1

## Slide 272: Use ADC in polling mode
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
  Select ADC IN13
4.1.1

## Slide 273: Use ADC in polling mode
Hardware connection
  Connect DAC out2 PA5 and ADC1 IN13 PC3 together
4.1.1

## Slide 274: Use ADC in polling mode
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parametr Settings
  Set ADC1
  Set sampling time for CH13
  Button OK
DAC from previous example
4.1.1

## Slide 275: Use ADC in polling mode
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.1.1

## Slide 276: Use ADC in polling mode
Start process ADC(same for DMA, DAC, TIM)
  Non blocking start process
Peripheral Initializations
Start Process
HAL_DAC_Start
Peripheral Initializations
Start Process
HAL_DAC_Start
4.1.1

## Slide 277: Use ADC in polling mode
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For DAC start use function
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_ADC_PollForConversion(ADC_HandleTypeDef* hadc, uint32_t Timeout)
  HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
DAC functions
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.1.1

## Slide 278: Use ADC in polling mode
Solution
  Variables
  DAC setup and start
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
uint32_t value_dac=0;
/* USER CODE END PV */
4.1.1

## Slide 279: Use ADC in polling mode
Solution
  Main loop with DAC set and ADC set
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_ADC_Start(&hadc1);
HAL_ADC_PollForConversion(&hadc1,10);
value_adc=HAL_ADC_GetValue(&hadc1);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095){
value_dac=0;
}
HAL_Delay(1);
}
/* USER CODE END 3 */
4.1.1

## Slide 280: Use ADC in polling mode
Test the functionality
  We need the address of variable value_adc
  This can be found usually in debug mode in watch, my address is 0x2000005C (depends on compilator and optimizations)
Start the STMStudio
  Set the ST Link SWD
  Right click into Display variable settings
  Select NEW
4.1.1

## Slide 281: Use ADC in polling mode
STM studio settings
  Set value_adc address my 0x2000005C
  Set 16bit unsigned val
  Right click on this line
  Select Send To VarViewer1
4.1.1

## Slide 282: Use ADC in polling mode
STM studio settings
  Viewers settings is on bottom
  Set the correct upper value to 4096(12bit)
4.1.1

## Slide 283: Use ADC in polling mode
STM studio settings
  Now press green play button
  And you will see content of value_adc
4.1.1

## Slide 284: 4.1.2 ADC Interrupt lab

## Slide 285: Use ADC with interrupt
Objective
  Learn how to setup ADC with interrupt in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in interrupt in CubeMX and Generate Code
  Learn how to start ADC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.1.2

## Slide 286: Use ADC with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F0 > STM32F030 > LQFP64 > STM32F030R8
4.1.2

## Slide 287: Use ADC with interrupt
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parametr Settings
  Set ADC1
  Set sampling time for CH13
  Button OK
4.1.2

## Slide 288: Use ADC with interrupt
CubeMX ADC configuration
  TAB>NVIC settings
  Enable ADC1 interrupt
  Button OK
4.1.2

## Slide 289: Use ADC with interrupt
CubeMX NVIC configuration
  Because we want use the Systick for delay in interrupt The ADC interrupt priority must be changed
  TAB>Configuration>System>NVIC
  Change ADC1 preemption priority to 1
4.1.2

## Slide 290: Use ADC with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.1.2

## Slide 291: Use ADC with interrupt
HAL Library ADC with IT flow
Start process with interrupt generation at end of process
HAL_ADC_Start_IT
ADCInitializations
including peripheral interrupt NVIC initializations
HAL_ADC_IRQHandler
process callback
HAL_ADC_ConvCpltCallback
process Error callback
HAL_ADC_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
ADC_IRQHandler
4.1.2

## Slide 292: Use ADC with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
For DAC start use function
  HAL_ADC_Start_IT(ADC_HandleTypeDef* hadc, uint32_t Channel)
  HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
ADC complete callback function
  HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
4.1.2

## Slide 293: Use ADC with interrupt
Solution
  Variables
  Start ADC
/* USER CODE BEGIN 2 */
HAL_ADC_Start_IT(&hadc1);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
/* USER CODE END PV */
4.1.2

## Slide 294: Use ADC with interrupt
Solution
  ADC complete callback routine
/* USER CODE BEGIN 4 */
void HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
{
value_adc=HAL_ADC_GetValue(&hadc1);
HAL_Delay(1);
HAL_ADC_Start_IT(&hadc1);
}
/* USER CODE END 4 */
4.1.2

## Slide 295: Use ADC with interrupt
STM studio settings
  Check functionality again with STMstudio
4.1.2

## Slide 296: 4.1.3 ADC with DMA lab

## Slide 297: Use ADC with DMA
Objective
  Use the DAC part from previous lab
  Learn how to setup ADC with DMA in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in DMA in CubeMX and Generate Code
  Learn how to start ADC and measure the DAC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.1.3

## Slide 298: Use ADC with DMA
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
  Select ADC IN13
4.1.3

## Slide 299: Use ADC with DMA
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parameter Settings
  Set ADC1
  Set sampling time for CH13
  DMA Continuous requests
  Button OK
DAC from previous example
4.1.3

## Slide 300: Use ADC with DMA
CubeMX ADC configuration
  TAB>DMA Settings
  Button ADD
  DMA request ADC1
  Peripheral to memory direction
  Circular mode
  Memory increment
  Half word data width
  Button OK
4.1.3

## Slide 301: Use ADC with DMA
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.1.3

## Slide 302: Use ADC with DMA
HAL Library ADC with DMA flow
Start process with interrupt generation at end of process
HAL_ADC_Start_DMA
ADCInitializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
process callback
HAL_ADC_ConvCpltCallback
process Error callback
HAL_ADC_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
DMA1_StreamX_IRQHandler
4.1.3

## Slide 303: Use ADC with DMA
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For DAC start use function
  HAL_ADC_Start_DMA(ADC_HandleTypeDef* hadc, uint32_t* pData, uint32_t Length)
DAC functions
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.1.3

## Slide 304: Use ADC with DMA
Solution
  Variables
  DAC setup and start ADC/DAC
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
HAL_ADC_Start_DMA(&hadc1,(uint32_t*)&value_adc,1);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
uint32_t value_dac=0;
/* USER CODE END PV */
4.1.3

## Slide 305: Use ADC with DMA
Solution
  ADC main routine
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095){
value_dac=0;
}
HAL_Delay(5);
HAL_ADC_Start(&hadc1);
HAL_Delay(5);
}
/* USER CODE END 3 */
4.1.3

## Slide 306: Use ADC with DMA
STM studio settings
  Check functionality again with STMstudio
4.1.3

## Slide 307: 6.1.1 Application IAP

## Slide 308: IAP using UART
Objective
  Learn how to setup IAP thru UART using CubeMX
Goal
  The purpose of this application note is to provide general guidelines for creating an IAP application on STM32 microcontrollers.
  The X-CUBE-IAP-USART firmware package is delivered with this document and contains the source code of IAP examples for STM32 microcontrollers
6.1.1

## Slide 309: IAP using UART
Principle
  When a reset occurs, the program counter is set to execute the IAP driver
  The condition is the user button key pressed
  When this condition is met, the IAP driver code executes a branch that updates the user application
  If this condition is not met, usually by default, executes this user application.
6.1.1

## Slide 310: IAP using UART
When the IAP driver directly launches the user application:
  1.The IAP driver sets the main stack pointer to the application address.
  2. The next instruction executes the jump (unconditional branching) to the application.
  3. The application then sets its own interrupt vector table as active
6.1.1

## Slide 311: IAP using UART
Flowchart
6.1.1

## Slide 312: Appendix A CubeMX install

## Slide 313: CubeMX install
CubeMX tool
  http://www.st.com/web/catalog/tools/FM147/CL1794/SC961/SS1533/PF259242?s_searchtype=partnumber
The CubeMX tool need the java
  Please check if you have actual java on your pc, for sure 32bit and 64bit version
Optionally you can download the Cube packages for STM32 device if you don’t want to download them throe CubeMX
  STM32CubeL0
  STM32CubeL1
  STM32CubeF0
  STM32CubeF2
  STM32CubeF3
  STM32CubeF4
A

## Slide 314: CubeMX install
Install the CubeMX
After installation run CubeMX
In case you download the package from web we need to find the place where they need to be stored
MENU>Help>Updater Settings…
You will see where is the repository folder
  Default is C:/User/Acc_name/STM32Cube/Repository/
You need to download STM32 packages into this folder
Or CubeMX automatically download them into this folder
A

## Slide 315: CubeMX install
The comparison of the CubeMX repository settings and structure in this folder
In case you want to download this files automatically use in CubeMX
  MENU>Help>Install New Libraries
  Select libraries which you want
  Force download with button Install Now
A

## Slide 316: CubeMX install
For the code generation the CubeMX use the package from the Repository folder
The CubeMX can generate the code for some GUI
  Keil
  IAR
  Atollic
For the debugging is necessity to have the ST-Link drivers
  STSW-LINK003 driver for Win XP/Vista/7
  STSW-LINK006 driver for Win 8
For driver installation you will need the Admin rights on your PC
A

## Slide 317: Appendix B Documents

## Slide 318: CubeMX documentation
CubeMX user manual UM1718
  http://www.st.com/st-web-ui/static/active/en/resource/technical/document/user_manual/DM00104712.pdf
CubeMX release note RN0094
  http://www.st.com/st-web-ui/static/active/en/resource/technical/document/user_manual/DM00104712.pdf
CubeMX technical note TN0072
  http://www.st.com/st-web-ui/static/active/en/resource/technical/document/technical_note/CD00214439.pdf
B

## Slide 319: STM32F429i-Discovery documentation
STM32F429i-Discovery page
  http://www.st.com/web/en/catalog/tools/FM116/SC959/SS1532/LN1848/PF259090?s_searchtype=keyword
STM32F429i-Discovery user manual with discovery schematics
  http://www.st.com/st-web-ui/static/active/en/resource/technical/document/user_manual/DM00093903.pdf
B